## Slide 1: Geotechnical Properties and Foundation Requirements of the Lunar Laser Ranger at Matjiesfontein Space Geodesy Observatory
Susan Bothma1, L Croukamp1
1. Department of Civil Engineering, University of Stellenbosch

## Slide 2: OUTLINE
What is an LLR?
Slope Stability Analysis
Geological Properties
Construction Risks

## Slide 3: What is a LLR?
What is a Lunar Laser Ranger (LLR)?
An LLR measures the distance between the Earth and the Moon using a laser. The laser projects to a reflector placed on the moon during the Apollo era. The reflector reflects the light back to the receiver and uses the recorded travel time to calculate the distance.
The LLR needs to be very stable to:
Point at the exact location on the moon and
Ensure accurate measurements.
To ensure stability, the following need attention:
Geotechnical investigations such as slope stability and geology of the Matjiesfontein Space Geodesy Observatory (MGO) site,
Risks during construction

## Slide 4: Slope Stability Analysis
To ensure that the ground on which the 7 ton LLR will be built is stable, a complete slope stability analysis needs to be done. The possible failures identified on the site were:

## Slide 5: Slope Stability Analysis
To determine the safety, data were collected in various ways. GPS survey was done to create a 3D model of the site and to analyse circular slip. A joint survey was done in two ways, a Breithaupt compass or an Android application: Rocklogger from RockGecko. This was used to analyse wedge and planar failure.
GPS
Rocklogger Application
Breithaupt compass

## Slide 6: Slope Stability Analysis
Slope stability analyses have been done at the following places:
Gravimeter Vault site (Susan Bothma),
Proposed site 1 for LLR (Deon Visser) and
Administrative buildings (Guillaume de Swart).

## Slide 7: Slope Stability Analysis
Studies have determined that these areas are safe to
Circular slip,
Toppling and
Wedge failure.
The only instability that may occur on the site is possible planar failure.
A retaining wall was designed for the administrative buildings site. A cantilever retaining wall will be the best solution.
Typical analysis of Circular- and Wedge-failure

## Slide 8: Geological Map
CPd
Cw
Cw
Cw
Cf
Ck
Dwi
Dwi
Ck
Ck
CPd – Dwyka formation
Cw – Waaipoort formation
Cf – Floriskraal formation
Ck – Kweekvlei formation
Dwi – Witpoort formation

## Slide 9: Construction Risks
Possible risks that may occur during construction period:
Early thermal shrinkage,
Construction quality,
Subsurface geological and geotechnical conditions,
Site access,
Availability of resources,
Productivity of labour, labour disputes or strikes,
Damage to persons or property or
Security of site.
The main concern during construction is early thermal shrinkage. Early thermal shrinkage is an exothermal reaction due to the hydrations of cement. This causes variations of temperature within the concrete, which then leads to cracking.

## Slide 10: Construction Risks
Possible risks that may occur during construction period:
Early thermal shrinkage,
Construction quality,
Subsurface geological and geotechnical conditions,
Site access,
Availability of resources,
Productivity of labour, labour disputes or strikes,
Damage to persons or property or
Security of site.
The main concern during construction is early thermal shrinkage. Early thermal shrinkage is an exothermal reaction due to the hydrations of cement. This causes variations of temperature within the concrete, which then leads to cracking.
Cracking as a Result of
Early Thermal Shrinkage

## Slide 11: Risks Management
Likelihood | Consequences |  |  |  | 
 | Insignificant (Minor problem easily handled by normal day to day processes) | Minor (Some disruption possible, e.g. damage equal to R5 million) | Moderate (Significant time/resources required, e.g. damage equal to R10 million) | Major (Operations severely damaged, e.g. damage equal to R100 million) | Catastrophic (Business survival is at risk, e.g. damage equal to R250 million)
Almost Certain (e.g. >90% chance) | High | High | Extreme | Extreme | Extreme
Likely (e.g. between 50% and 90% chance) | Moderate | High | High | Extreme | Extreme
Moderate (e.g. between 10% and 50% chance) | Low | Moderate | High | Extreme | Extreme
Unlikely (e.g. between 3% and 10% chance) | Low | Low | Moderate | High | Extreme
Rare (e.g. <3% chance) | Low | Low | Moderate | High | High

## Slide 12: Acknowledgements
I would like to thank
Leon Croukamp,
Deon Visser,
Guillaume de Swart and
Inkaba yeAfrica.

## Slide 13: Questions?