## Slide 2
Structural Biology at the ESRF: present and future
Gordon Leonard
(on behalf of)
ESRF Structural Biology Group

## Slide 3: Hierarchical length scales in biology
Figure adapted from Bărbulescu, R. & Ioan, D. (2015). Multi-scale and reduced modelling of biological systems. 9th International Symposium on Advanced Topics in Electrical Engineering (ATEE); DOI: 10.1109/ATEE.2015.7133876
Structural/Molecular Biology

## Slide 4: Structural/Molecular Biology
Introduction to Protein Structure, C-I. Branden & John Tooze, Garland Publishing Inc., 1991

## Slide 5: ESRF Facilities for (Integrated) structural Biology
ID23-1, ID23-2
ID29
MASSIF-1, MASSIF-3, ID30B
BM29 (BioSAXS)
CM01 cryo-EM
iCoS
High Pressure Cryo-cooling
Sample storage
8 end-stations:
6 MX
1 Cryo-EM
1 BioSAXS
iCoS
HP Cryo-Cooling
CIBB

## Slide 6: SB@ESRF PRE-EBS: versatile, complementary end-stations
 | 1st Operation | Energy [keV] | Beam size [mm2] | Flux [ph/s] | Diffractometer | Detector | Sample Changer | Experiments
ID29 | 2000 | 6-20 | 10-50 | 5x1012 | MD2 | Pilatus 6M | FlexHCD | MAD/SAD; MDX; on-line Raman, UV
ID23-1 | 2004 | 6-20 | 10-40 | 3x1012 | MD2M | Pilatus 6M | FlexHCD | MAD/SAD; MDX; dehydration
ID30B | 2015 | 6-20 | 20-200 | 1013 | MD2-S | Pilatus3 6M | FlexHCD | MAD/SAD; MDX; dehydration; in situ
MASSIF-3 | 2015 | 12.8 | 15 | >2 x 1013 | MD2-S | Eiger 4M | FlexHCD | Mini-focus; MDX; SSX; on-line UV
ID23-2 | 2006 (2017) | 14.2 | 5 x 7 (2 x 2) | 1x1012 | MD3Up | Pilatus3 2M | FlexHCD | Microfocus; SSX
MASSIF-1 | 2014 | 12.8 | 50 (20-150) | 2x1012 | RoboDiff | Pilatus3 2M | RoboDiff | Automatic data collection; Mail-in; fragment screening, etc.
BM29 | 2011 | 7–15 | 500 × 500 | 1.3x1013 | N/A | Pilatus 1M | ARINAX liquid handler | BioSAXS; SEC-SAXS
CM01 | 2017 | Electron Microscopy |  |  |  |  |  | Single particle reconstruction

## Slide 7: MX Beamlines: Diffraction data for more than 15,000 PDB Depositions: How?
User-friendly
  Web-based MXCuBE3 User Interface
    MXCuBE Collaboration
Very high level of automation
  MD2 diffractometeters
  Flex-HCD sample changers
  Constant monitoring of flux on sample allows proper experiment design (radiation damage)
  Beamline expert system
    Workflows (beamline ‘Wizards’)
      MXPress workflows
      X-ray centering of samples
      Diffraction cartography
      Set up and execution of helical data collections
      Multi-crystal data collection (i.e. MeshandCollect)
      Dehydration protocols
      Radiation damage
    …..
Display and download of results at all stages of experiment
  ISPyB/Exi
    Automatic data processing
    Automatic structure solution (SAD, Molecular Replacement)
      ISPyB Collaboration

## Slide 8: Automation + MxCuBE + ISPyB = Remote Access/Mail-in
For mail-in/remote access ESRF pays for sample transport to/from Grenoble
Notes: Graphical overview of the automated characterization and data-collection process running on MASSIF-1. All steps in the process are shown. The beamline-control GUI MXCuBE takes care of sample mounting/unmounting and optical centring of the sample mount. Information about the samples, dewar tracking and the presentation of results are via the beamline LIMS system ISPyB. The software described here starts once a sample has been mounted and optically centred to the X-ray beam. [Svensson, O., Malbet-Monaco, S., Popov, A., Nurizzo, D. and Bowler, M. W. (2015). Acta Cryst. D71, 1757-1767. doi:10.1107/S1399004715011918]

## Slide 9: ISPyB/Exi Display and download of results (MXPRESSE Workflow)
Off-line reprocessing coming soon….

## Slide 10: Automatic Structure determination
Automatic ligand fitting coming soon.

## Slide 11: A versatile sample environment Allows less standard experiments
In situ Plate screening
In Situ-1TM ; Crystal DirectTM ; CrystalQuickTM X
Crystal dehydration

## Slide 12: small crystals require Multi-crystal data collection: MDX & SSX:
Chart: Crystal size, µm
| 1 | 1.56 | 2 | 3 | 5 | 7 | 10 | 15 | 20 | 25 | 30 | 40 | 50 | 75 | 100
 | 4.9 | 3.83 | 3.28 | 2.78 | 2.16 | 1.95 | 1.77 | 1.61 | 1.51 | 1.47 | 1.42 | 1.34 | 1.28 | 1.25 | 1.2
Complete data set resolution vs. crystal size
Chart: Crystal size, µm
| 1 | 2 | 3 | 5 | 7 | 10 | 15 | 20
 | 24750 | 4888 | 1100 | 220 | 90 | 40 | 11 | 1
 | 990 | 158 | 50 | 6 | 1
Number of cryocooled crystals of a given size required to achieve dataset resolutions of dmin = 1.5 Å (blue) and dmin= 2.0 Å (orange).
Radiation damage means that the resolution of a complete data set that can be collected from a single crystal is (size) limited.
Can overcome this limitation by collecting (and merging) partial data sets from many crystals
For a Thermolysin crystal (Space Group P6122; B-factor=11.5 Å²) 1x1x1 mm3 in dimensions partial data sets from about 15000 crystals would be needed to achieve a final data set resolution of dmin = 1.5 Å (A. Popov, ESRF).
Multi-crystal data collection/‘Serial’ crystallography the only way to do this efficiently.
Notes: 12

## Slide 13: SSX & MDX at the ESRF: Room and Cryo-temperatures

## Slide 14
Techniques complementary to MX

## Slide 15: BM29 Biosaxs: Sample changer + HPLC system
Samples stored in 96 well plates, PCR tubes
Thermo-regulation storage: 4-40ºC, exposure cell: 4-60ºC
Sample loading and cleaning: 30’
HPLC system mostly used in isocratic elution mode
(mobile phase composition is kept constant and uniform
ROBOT
Switch between
SC and SEC modes
quick and robust

## Slide 16: THE RISE OF BIOSAXS
Chart: 
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
 | 6 | 11 | 15 | 36 | 27 | 11 | 7 | 2 | 2
 | 1 | 17 | 53 | 64 | 80 | 97
 | 1 | 3 | 4 | 3 | 2
First BioSAXS users at ID14-3
in November 2008
ID14-3 closed in December 2011
First BioSAXS users at BM29
in June 2012
ID14-3 = 117
BM29 = 324
both = 13
ROBOT
PILATUS
ADDAPTED OPTICS
HPLC online
Complete refurbishment during ESRF-EBS

## Slide 17: CM01: BRINGING THE CRYO-EM ‘RESOLUTION REVOLUTION’ TO THE ESRF USER COMMUNITY
Titan Krios G3
300 kV
Quantum LS energy filter
K2 summit direct detector
Volta phase plate
On-line: November 2017
Rolling proposal
BTAP evaluation
Approved proposal
Pre-evaluated project
(sample preparation
established)
Grids
available
Grids NOT
available
KRIOS
KRIOS
GRID preparation
@ ESRF cryoEM lab

## Slide 18: HOW ACCESS TO CM01 WILL EVOLVE: THE PSB CRYO-EM PLATFORM

## Slide 19: CM01: INITIAL RESULTS FROM TOBACCO MOASIC VIRUS
CM01 is operating during ESRF-EBS shutdown

## Slide 20: In crystallo optical spectroscopy (Icos)

## Slide 21: In crystallo optical spectroscopy (Icos)

## Slide 22: HIGH-PRESSURE CRYO-COOLING
- Cool crystals without cryoprotectant
- Improve diffraction quality (lower mosaicity)
- where do ligands bind?
- where is O2/NO/… entering/leaving
~2 kbar
Non-cryprotected Trypsin
-No ice rings
-High resolution 1.07Å
Low mosaicity 0.078
Rsym 5.3%
-Rwork /free 10.9/13.4
P. van der Linden et al. (2014) J. Appl. Cryst. 47, 584-592.

## Slide 23: Esrf-ebs: faster & better WITH SMALLER, MORE INTENSE x-RAY BEAMS
Where? – What? – Optimise? – Trash?
Smaller beam = finer sampling
Microcrystals
100mm
Bowler et al. & Leonard , Acta Cryst. (2010). D66, 855–864
Large crystals
Where is ‘sweet spot’?
Smaller beam = finer sampling
MDX
SSX
‘Standard’ MX / Fragment Screening
Notes: 23

## Slide 24: Room Temperature Data Collection (SSX/MDX) and Pump-probe investigations
Crystal structures obtained at cryogenic temperatures can obscure functionally important conformations: i.e. for small GTPase H-ras only the RT structure showed the catalytically essential glutamine residue in the conformation that is required for GTP hydrolysis.
Fraser et al., PNAS 108, 16247-16252, 2011
Because of radiation damage, serial crystallography is (probably) the only route to obtaining RT structures.
A. Pearson, ESRF UM2016
Room-temperature Data Collection
Pump-probe in crystallo
Notes: Mutations in H-Ras paralogs in H3 are involved in cancers supporting idea that this network is critical for function.
The allosteric network involved had been suggested by NMR.

## Slide 25: EBSL8 - A beamline for (time-resolved)serial crystallography
High flux (1016 ph/s), large bandwidth (~1%)
Beamsize: 0.5 mm – 10 mm
Tuneable: 10-30 keV
iCOS

## Slide 26: time-resolved crystallography experiment performed at an XFEL
Study of the photocycle of the membrane protein bacteriorhodopsin (Nango, Royant et al., Science, 354, 1552-1557, DOI: 10.1126/science.aah3497)

## Slide 27: Time-RESOLVED MX AT esrf: A PHOTORECPTOR PHOTOCYCLE (Signalling in Phototropism)
CCcluster: Santoni, G., et al., (2018). J. Appl. Cryst. 50, 1844-1851.
100 complete data sets (1000 images) from 100 different crystals
Each complete data set divided into 66 sub-wedges of 15 images (60msec)
HCA clustering of 100 sub-data sets for each time point
66 complete data sets (time points) with time resolution of 60 msec
time constant ~90 ms
S. Aumonier, A. Royant. G. Santoni, G. Leonard et al. unpublished.
Improved experimental set-up (w axis rotation of 720o/second)
Different clustering technique (i.e. Genetic Algorithm, (Acta Cryst. D72, 1026)).
~1msec time resolution?

## Slide 28: Movie of adduct formation

## Slide 29: SB@ESRF POST-EBS: versatile, complementary end-stations
 | 1st Operation | Energy [keV] | Beam size [mm2] | Flux [ph/s] | Diffractometer | Detector | Sample Changer | Experiments
ID29 | 2021 | 10-15 [35] | 0.5 x 0.5 [10 x 0.5] | 1x1016 | MD3Up-SSX | JungFrau 4M | N/A | (TR-)SSX
ID23-1 | 2004 (2021) | 6-20 | 10-40 | 3x1012 | MD2-S | Eiger 2 16M CdTe | FlexHCD | MAD/SAD; MDX; dehydration
ID30B | 2015 | 6-20 | 20-200 | 1013 | MD2-S | Pilatus3 6M | FlexHCD | MAD/SAD; MDX; dehydration; plates
MASSIF-3 | 2015 | 12.8 | 15 | >2 x 1013 | MD2-S | Eiger 4M | FlexHCD | Mini-focus; MDX; SSX; on-line UV
ID23-2 | 2006 (2017) | 14.2 | (1 x 1) | 1x1013 | MD3Up | Pilatus3 2M | FlexHCD | Microfocus; SSX
MASSIF-1 | 2014 (2021) | 12.8 | 50 (10-100) | 1x1013 | MD2-S | Pilatus3 2M | FlexHCD | Automatic data collection; Mail-in; fragment screening, etc.
BM29 | 2012 (2020) | 7–15 | 500 × 500 | 5x1013 | N/A | Pilatus 2M in vacuuo | ARINAX liquid handler | (TR-)BioSAXS; SEC-SAXS
CM01 | 2017 | Electron Microscopy |  |  |  |  |  | Single particle reconstruction (tomography, ED)

## Slide 30: Some recent highlights from SB FACILITIES at The ESRF
Molecular basis for high-affinity agonist binding in GPCRs. Science 364, 775-778 (2019).
A class of highly selective inhibitors bind to an active state of PI3Kγ. Nat. Chem. Biol. 15, 348-357 (2019).
Structural Basis of Transcription: RNA Polymerase Backtracking and Its Reactivation, Molecular Cell, 75, 298-309.e4 (2019).
Structural Principles in Robo Activation and Auto-inhibition. Cell, 177, 272-285.e16 (2019).
A kiwellin disarms the metabolic activity of a secreted fungal virulence factor. Nature 565, 650-653 (2019).
Polyclonal and convergent antibody response to Ebola virus vaccine rVSV-ZEBOV. Nature MedIcIne 25, 1589–1600 (2019).
Thank you for your attention!

## Slide 31: Acknowledgements
ESRF
Jean Susini
Harald Reichert
Gordon Leonard
Christoph Mueller-Dieckmann
Sasha Popov
Max Nanao
Daniele de Sanctis
Petra Pernot
Mark Tully
Didier Nurizzo
(David von Stetten)
Isai Kandiah
David Flot
(Stephanie Monaco)
Montserrat Soler Lopez
(Guillaume Gotthard)
Gianluca Santoni
(Nicolas Foos)
(Gabriele Giachin)
Igor Melnikov
(Slyvain Aumonier)
Maksim Rulev
Romain Bouverot
Hadrien Depernet
EMBL Grenoble
Stephen Cusack
Andrew McCarthy
Matthew Bowler
(Martha Brennich)
(Uli Zander)
Shibom Basu
Florent Cipriani
Franck Felisaz
Robert Janocha
Marcos Lopez-Marrero
Gergely Papp
Christopher Rossi
Jeremy Sinoir
Clement Sorez
EMBL Hamburg
Gleb Bourenkov
IBS
Winfried Weissenhorn
Guy Schoen
Gregory Effantin
Philippe Carpentier
Antoine Royant
ESRF
Hugo Caserotto
Fabien Dobias
Thierry Giraud
Mario Lentini
John Surr
Jonathan Gigmes
Samira Accajoui
Ulrike Kapp
Deborah Davison
Pascal Theveneau
Carole Clavel
Peter van der Linden
Antonia Beteva
Matias Guijarro
Olof Svensson
Alejandro de Maria
Solange Delageniere
Marcus Oskarsson
ILL
Trevor Forsyth
Traore