## Slide 1
Gaol.
Studying the Absorption & Scattering of PET Photons in Medical & Mineral PET
Prince Nqobizitha Ncube
10 October 2025

## Slide 2: Backgroundjj
PRESENTATION CONTENTS
Background
Rationale for conducting the project
PET and MinPet
Project Aim
Simulation Setup
Simulation Results
Experimental results

## Slide 3
PET Background
Radioactive material similar to glucose is injected in a body.
It releases positrons.
Annihilation
Detectors detect the photons.
Algorithm creates a 3D reconstruction.
Primarily used in:
: tumor detection.
: Assessing myocardial perfusion and viability.
: diagnosis of epilepsy & Alzheimer's disease
Figure 1.1

## Slide 4
Adaptation To MinPet
Reduces barren rock processing
Avoids accidental diamond crushing
Rapid detection (<20 s per decision)
Reducing sediment runoff
Energy Use Reduction
Elimination of exploitative labour (in manual processing
Figure 1.2
Figure 1.3(a)
Figure 1.3(b)

## Slide 5
Photon Interaction
Photoelectric effect – photon is absorbed. photoelectron released.
Compton scattering – photon transfers some energy and knocks off electron. Photon deflected.
Pair Production – Due to photon-nucleus interaction. A positron-electron pair formed (1.022 MeV threshold)
511 keV photons primarily interact via Compton scattering & photoelectric effect.
Figure 1.4

## Slide 6
No standard reference exists for kimberlite - photon interaction
We must understand how signal is influenced kimberlite
This helps optimize detector placement and shielding.
Supports MinPet development
Why Study this Photon Behavior?
Annihilation
Photon Passage through material
Detector
Image Reconstruction
Contrast ?

## Slide 7
To study how PET photons behave in kimberlite slabs
Through
Comparing measured and GEANT4 simulated absorption and scattering
Project Aim

## Slide 8
Key Variables
Type | Variable
Control Variables | Photon energy
 | Detector type and position
 | Source-detector distance
 | Kimberlite composition
 | Simulation model
Independent Variable | Kimberlite slab thickness
Dependent Variables | Photon count rate at detector
 | Energy spectrum at detector
 | Attenuation coefficient (μ)

## Slide 9
Positrons from Na-22 annihilate with diamond electrons
511 keV photons emitted in all directions.
Photons interact with kimberlite
What we measure at the detector informs us how the material affects the signal.
Simulation
Figure 1.5
Figure 1.6

## Slide 10
Simulation Results
Chart: Simulated Data
| 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
 | 136124 | 108421 | 91239 | 65987 | 54510 | 42505 | 31870 | 26586 | 20500 | 15150 | 10659
Linear attenuation coefficient
μ = − ()
I = Ioe-μx
µsimulation = 24.96 ± 0.62 m -1
Figure 1.7

## Slide 11
Experimental Setup
Figure 1.7
Random Experimental deviate for 10000 counts

## Slide 12
Experimental Results
511 keV Peak
Figure 1.8

## Slide 13
Experimental Results
Chart: Count Rate
| 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 7.0000000000000007E-2 | 0.1
I(Counts/s) | 2.9507 | 2.2237 | 1.8619 | 1.4251 | 1.2558 | 1.0155 | 0.69396 | 0.40225
µexperimental = 19.56 ± 0.51 m -1
Figure 1.8

## Slide 14
Theoretical coefficient Benchmarking
Theoretical linear attenuation coefficient Calculation:
μ=ρ ∑​wi​ ()i
Kimberlite Density = [ 2.5 – 3.1 ]
Theoretical | [21.65 m⁻¹ , 26.85 m⁻¹] | Benchmarking
Experimental | 19.56 ± 0.51 | Not in range
Simulation | 24.96 ± 0.62 | In range
Mass attenuation coefficient (
Sources of Experimental Error:
a) Hand-Sawn Slabs
b) Concentric Alignment:
Figure 1.9

## Slide 15
Conclusion
Aim: To study how PET photons behave in kimberlite slabs
Result: No confluence of the 3 values of linear coefficient of attenuation
Although there is not confluence, this is still a valuable study.
Recommendations: Future study utilizing more accurate machining methods.
Improve alignment using a laser
Measure the density of all the slabs and adjust for the density.

## Slide 16
THANK YOU!
QUESTIONS ?