## Slide 1: Geophysical Survey Methods in the Southern Karoo Basin
Martin Bentley
Lucian Bezuidenhout
Part of SHALE GAS WORKSHOP
1st OCTOBER 2014

## Slide 2: Scope
Overview – Airborne – Seismic – Magneto-Telluric - Conclusion

## Slide 3: Defining Geophysics
Measure the physical response of rocks
Can be linked to specific rock properties
Overview – Airborne – Seismic – Magneto-Telluric - Conclusion

## Slide 4: Advantages of geophysical surveys
Not limited to areas with outcrop
Regional scale
Well-established techniques
  Exploration
  Civil engineering
Overview – Airborne – Seismic – Magneto-Telluric - Conclusion

## Slide 5: Geophysics in the Karoo
Some work has been done
  Limited scale
  Raw data is often not freely available
Importance of the Karoo is growing
  Need more subsurface data
Overview – Airborne – Seismic – Magneto-Telluric - Conclusion

## Slide 6: Overview of proposed methods
Airborne Survey
  Magnetic
  Gravity
  Radiometric
Passive seismic tomography
Magneto-Telluric Survey
Overview – Airborne – Seismic – Magneto-Telluric - Conclusion

## Slide 7: The Airborne Survey
Martin Bentley

## Slide 8: Background
Currently a lack of high-resolution data
  Magnetic
Data is not freely available
  Radiometric
  Gravity
Overview – Airborne – Seismic – Magneto-Telluric - Conclusion

## Slide 9
Overview – Airborne – Seismic – Magneto-Telluric - Conclusion

## Slide 10
Overview – Airborne – Seismic – Magneto-Telluric - Conclusion

## Slide 11: Proposed Plan
Use gyrocopter as payload carrier
Gather multi-parameter data
  Magnetic
  Gravity
  Radiometric
  Data for accurate digital terrain model
Overview – Airborne – Seismic – Magneto-Telluric - Conclusion

## Slide 12: The Payload Carrier
Overview – Airborne – Seismic – Magneto-Telluric - Conclusion
Gyrocopters in Barberton, courtesy M. Doucouré.

## Slide 13: Data processing
Existing software is:
  Expensive
Will create software for:
  Processing
  Analysis
  Visualisation
Overview – Airborne – Seismic – Magneto-Telluric - Conclusion

## Slide 14: The Passive Seismic Survey
Lucian Bezuidenhout

## Slide 15: Potential Karoo areas for exploration for SHALE GAS
Map of South Africa showing possible areas of future exploration and associated companies with pending exploration rights
ANGLO
SASOL
SHELL
FALCON
BUNDU
GREAT KAROO
G. Steyl and G. J. van Tonder [http://dx.doi.org/10.5772/56310]

## Slide 16: Objectives
Explore the concept of passive seismic tomography using three-component sensors on a seismic grid.
Create a 3-D imagery of the Karoo sub-surface using passive seismic measurements.
Gain an improved understanding of the subsurface of the Karoo basin.
Construct a seismic (earthquake) survey of the Karoo prior to hydraulic fracking.
To complement and support other investigated geophysical aspects (e.g. hydrology, geology, etc…) with microseismic activity monitoring.
Go into areas with limited accessibility.
Overview – Airborne – Seismic – Magneto-Telluric – Conclusion

## Slide 17: Where in the Karoo?
Overview – Airborne – Seismic – Magneto-Telluric – Conclusion

## Slide 18: Seismic Tomography vs Passive Microseismic Monitoring
Microseismic monitoring – passive observation of very small earthquakes which are naturally occurring underground or are present as a result of human activities (i.e. imaging subsurface using subsurface source +).
Passive imaging techniques are based on ability to extract coherent contribution to seismic field from continuous ambient noise signal (based on reconstruction of Green’s function cross-correlation of data acquired at two different locations *).
AREAS of APPLICATION :
Probing of Earth’s interior with noise – information from upper and middle crust can be retrieved with increased spatial resolution.
Detection and characterization of changes within active structures.
(e.g. volcanoes, faults, earthquake zones, glaciers)
Mining, Oil and Gas, Shale Gas, Geothermal Reservoirs, Stability of Nuclear Waste and CO2 Repositories# [exploration, risk management and mitigation, environmental concerns, gain knowledge of existing fault and fracture networks, continuous monitoring, etc.]
+ Claerbout, Geophysics, 33 (1968) 264. * Shapiro and Campillo, Science, 307 (2005) 1615.
# Case studies: Sabra et al., Geophysi. Res. Lett., 32 (2005) L14311; Stehley et al., Geophys. J. Int., 178 (2009) 338; Lin et al., Geophys. J. Int., 170 (2007) 649.
Overview – Airborne – Seismic – Magneto-Telluric – Conclusion

## Slide 19: Advantages
OPERATIONAL
  - can concentrate in regions of interest as well as large areas
  - can obtain data from difficult terrain
  - no day-to-day operational costs
  - can create community involvement
ENVIRONMENTAL
  - uses underlying perturbations as a “source” signal
  - no explosives, no drilling, no cables….
  - suitable for environmentally sensitive regions
Can conceivably be used in frontier geopolitical and sensitive exploration areas and to establish regional baselines.
Overview – Airborne – Seismic – Magneto-Telluric – Conclusion

## Slide 20: Technique Basics
Passive microseismic measurements can be carried out without synthetic sources or waiting for earthquakes
Resolution can be improved by increasing number of recording stations or periodic redeployment of stations
Accuracy and resolution of the subsurface image relies strongly on the ability to resolve the velocity model and upon density of sampling.
Sampling depth
up to 30 km
local seismic events
(magnitudes from -1 to 2 on RS)
Surface
Areas lacking sampling
Data
monitoring
Battery
Data Cube
Geophone
GPS
Overview – Airborne – Seismic – Magneto-Telluric – Conclusion

## Slide 21: Data Interpretation
Overview – Airborne – Seismic – Magneto-Telluric – Conclusion

## Slide 22: Previous model of Karoo
Overview – Airborne – Seismic – Magneto-Telluric – Conclusion
(Lindeque et al. (2007/8))

## Slide 23: The Magneto-Telluric Survey
Geophysical method used for imaging of subsurface by measuring natural variations of electric and magnetic fields at the Earth’s surface.
Energy source: solar energy and lighting cause variations in the earth’s magnetic field thus inducing electric currents (telluric currents) below the surface.
Different rocks, sediments and geological structures have different conductivities
Depths from 300 m to hundreds of km can be investigated; frequency range 0.0001 up to 10000 Hz.
Overview – Airborne – Seismic – Magneto-Telluric – Conclusion

## Slide 24
Resistivity model
EM wave propagation
Resistivity of Rocks
Overview – Airborne – Seismic – Magneto-Telluric – Conclusion

## Slide 25: Conclusion
This geophysical survey will aim for an increased understanding of the subsurface conditions in the Karoo by:
  Gathering new, high resolution data for critical areas
  Correlation of multiple geophysical methods
Hope to get better understanding of:
  Geological structures (folds/faults/intrusions)
Overview – Airborne – Seismic – Magneto-Telluric – Conclusion
Thank you